## Slide 1: Rain Gardens: A Simple Way to Do Your Part A Quick Commercial from the Rutgers Cooperative Extension Water Resources Program
E-mail: obropta@envsci.rutgers.edu
www.water.rutgers.edu

## Slide 2
Keep the Rain from the Drain
Notes: This rooftop is directly connected to the street. The rooftop runoff flows to the road to the catch basin to the stream. This rooftop is directly connected to the stream.

## Slide 3: Disconnect with a Rain Garden
Notes: Disconnect the rooftop to a rain garden.

## Slide 4: Rain Gardens
A rain garden is a landscaped, shallow depression that is designed to capture, treat, and infiltrate stormwater at the source before it becomes runoff.
Notes: What is a rain garden?

## Slide 5
Parts of a Rain Garden
Notes: 5
A rain garden has a flat bottom and fills up with stormwater runoff that slowly seeps into the soil.
5

## Slide 6: Rain Gardens
  Landscaped areas that treat stormwater runoff
  Designed to merge two important goals: aesthetics and water quality
  Can be blended into the landscape and made to look natural
  Water is directed into them by pipes, swales, or curb openings
Notes: More about rain gardens.

## Slide 7: Site Selection
Next to a building with a basement, rain garden should be located at a minimum of 10′ from building; no basement, 2′ from building
Do not place rain garden within 25′ of a septic system
Do not situate rain garden in soggy places where water already ponds
Avoid seasonably-high water tables within 2′ of rain garden depth
Consider flat areas first – easier digging
Avoid placing rain garden within dripline of trees
Provide adequate space for rain garden
Notes: Siting considerations.

## Slide 8: Native Vegetation
Notes: We plant our rain garden with native plants.

## Slide 9
Notes: The Blue House Picture. Before and after a roadside rain garden. Talk about increasing property value!

## Slide 10
Notes: Volunteers building a rain garden at elementary school in Cranford, NJ

## Slide 11
Notes: Beautiful rain garden at the Fanwood Public Library

## Slide 12
Notes: The crescent moon rain garden at the Woodbridge Health Department

## Slide 13
Notes: A shady area can be perfect for a rain garden.

## Slide 14
Notes: More native plants.

## Slide 15
Notes: Provides wildlife habitat

## Slide 16
Notes: Are more aesthetically pleasing than conventional detention basins

## Slide 17
Notes: Can be incorporated into the landscapes of individual homes

## Slide 18
Notes: Sequesters carbon – nice addition to the parking lot

## Slide 19
Notes: Rain garden at the Hillsborough Municipal Building

## Slide 20
Here is the website for the rain garden manual: http://www.water.rutgers.edu/Rain_Gardens/RGWebsite/RainGardenManualofNJ.html
Notes: We have a rain garden manual that is available for download from our website.

## Slide 21
Notes: We worked with UCONN to develop a rain garden app for New Jersey.

## Slide 22: Christopher C. Obropta, Ph.D., P.E. E-mail: obropta@envsci.rutgers.edu www.water.rutgers.edu